## Slide 1: On Becoming a Leader in Risk Management
1
Fundamentals of RM
RM System and Process
Applications & Perspectives
People & Org.
Incident Investigation
RM Tools & Challenges
Leadership in RM
RM in Industry
ENGG404 - Lecture
Chapter 2.3
Hazards and Hazard Identification
Notes: ENGG404 Lecture 00 - Day 1
2012 Fall
1
1

## Slide 2
Learning Outcomes of this Module:
Differentiate between a hazard, the severity of hazard, and consequences (impact on PEAP).
Describe and explain different types of hazards in terms of losses (including occupational and/or process safety), and the impact of the severity of those hazards.
Apply two different methods for identifying hazards associated with an activity.
2
Chapter 2.3: Hazard Identification
Notes: 2

## Slide 3
Based on knowledge of the inspector (the person looking for the hazards) and/or documented check-lists for use during an inspection.
Fuming sulfuric acid (corrosive material)
Weakened steel structures (corroded material)
Ground fault
Unbalanced rotating / reciprocating equipment
Slumping Walls
Moving equipment and desire to gain access (think: conveyor)
3
How We Identify Hazards: The Knowledge-Based Approach
Chapter 2.3: Hazard Identification
Notes: 3

## Slide 4
It follows that by mitigating one or more of these components of incident cause, incidents can be prevented.
Note: This technique can be applied for finding both occupational safety hazards AND process safety hazards!
4
How We Identify Hazards: The Discovery Approach, using one of our Two Models
Any combination of …
Energy (controlled or uncontrolled release or protected / unprotected source), and
Line-of-Fire (intentional or not intentional), and
Lack of Safeguard
… will result in an injury incident.
Any combination of …
Energy (controlled or uncontrolled release or protected / unprotected source), and
Line-of-Fire (intentional or not intentional), and
Triggers
… will result in an injury incident.
Chapter 2.3: Hazard Identification
Notes: 4

## Slide 5
Rephrase the components:
Find the Energy Source: mechanical, electrical, chemical, etc.
Look for the Line-of-Fire: bodies, assets, and environment that could be harmed by a release of the energy source.
Look for No/Inadequate Safeguards: the absence of the barrier or control measure or safeguard that is preventing or limiting or controlling exposure to the energy source.
Find the Trigger: the circumstances or mechanisms that will cause the release of the energy source.
Hazards become evident.
A sharp observer can see hazards that may not be obvious.
Then can take steps to address the hazard and avoid an incident.
Effectively working to eliminate the immediate causes of incidents
5
The Discovery Approach
Chapter 2.3: Hazard Identification
Notes: 5

## Slide 6
6
Hazards are associated with:
  activities,
  occupational losses
  process safety losses
Hazards are often related to substandard conditions and substandard work practices.
Context is important where there is a need to differentiate between a hazard, severity of hazard, and a consequence
We employ two approaches for identifying hazards:
  Knowledge based
  Discovery based.
Chapter 2.3: Hazard Identification
Summary
Notes: 6