## Slide 1: On Becoming a Leader in Risk Management
ENGG 404 - Lecture
Chapters 4.4, 4.5, and 4.6
The Relationship Between Latent Causes & Incidents
Linking Latent Causes to Recommendations for Action
Developing & Prioritizing Recommendations
1
Fundamentals of RM
RM System and Process
Application and Perspectives
People & Org.
Incident Investigation
RM Tools & Challenges
Leadership in RM
RM in Industry
Notes: ENGG404 Lecture 00 - Day 1
1
1

## Slide 2
2
Explain the components of the Swiss Cheese Model of a loss incident.
Explain how to “make the link” from latent causes to recommendations for actions.
Link a latent cause to a management system element and create a recommendation.
Ensure that recommendations address/eliminate latent causes.
Generate and prioritize recommendations for action.
Learning Outcomes of these Chapters:
Chapter 4.4: The Relationship Between Latent Causes & Incidents Chapter 4.5: Linking Latent Causes to Recommendations Chapter 4.6: Developing & Prioritizing Recommendations
Notes: 2

## Slide 3
Chapter 4.4:
The Swiss Cheese Model of a Loss Incident
3
Notes: ENGG404 Lecture 00 - Day 1
2012 Fall
3
3

## Slide 4
  The Block of Swiss Cheese and the Slices:
    The Risk Management Program
      Risk Management System
      Engineering Controls
      Administrative Controls
      Work Practices
Introduction – Examine The Components of the RM Program:
Chapter 4.4: The Swiss Cheese Model of a Loss Incident

## Slide 5
Consider the block of cheese and the set of cheese slices as your facility’s Risk Management Program.
The slices of cheese are successive safeguards (i.e. control measures, control mechanisms or barriers) to prevent a loss incident.
If the safeguards are deficient, as depicted by “holes”, an incident will occur.
The “Swiss Cheese” Model of a Loss Incident:
A Fresh Perspective: The Block of Swiss Cheese
Chapter 4.4: The Swiss Cheese Model of a Loss Incident

## Slide 6
Now consider the red arrow, wherein some kind of activity is planned, with its inherent hazards and risks and with the intention of a successful outcome.
The “Swiss Cheese” Model of a Loss Incident:
Planned activity and its hazards & risks …
and a successful outcome is intended.
A Fresh Perspective: The Block of Swiss Cheese
Successful outcome?
Chapter 4.4: The Swiss Cheese Model of a Loss Incident

## Slide 7
The Risk Management Program is applied (1,2,3,4) to control the hazards and reduce the risks associated with the planned activity to an acceptable level; where: 1) Risk Management System; 2) Engineering Controls; 3) Administrative Controls; 4) Work Practices.
The “Swiss Cheese” Model of a Loss Incident:
3
4
2
1
Planned activity and its hazards & risks
X
X
X
X
Successive levels of effective control measures
D
Successful outcome
A Fresh Perspective: The Block of Swiss Cheese
Chapter 4.4: The Swiss Cheese Model of a Loss Incident

## Slide 8
Risk Management System Elements(where weaknesses in these are latent causes)
Engineering Controls (engineering systems in design, construction, operation, maintenance)
Administrative Controls (documented procedures – what workers are supposed to be doing), and
Work Practices (what workers are actually doing).
The “Swiss Cheese” Model of a Loss Incident:
3
4
2
1
Planned activity and its hazards & risks
X
X
X
X
Successive levels of effective control measures
D
Successful outcome
A Fresh Perspective: The Block of Swiss Cheese
Chapter 4.4: The Swiss Cheese Model of a Loss Incident

## Slide 9
When the risk management program is implemented effectively, i.e. all safeguards and control measures are working, then there is a successful outcome to the planned activity, and loss incidents are prevented.
The “Swiss Cheese” Model of a Loss Incident:
3
4
2
1
Planned activity and its hazards & risks
X
X
X
X
Successful outcome
Successive levels of effective control measures
A Fresh Perspective: The Block of Swiss Cheese
Chapter 4.4: The Swiss Cheese Model of a Loss Incident

## Slide 10
The implementation of a Risk Management Program maintains the effectiveness of all control measures.
The “Swiss Cheese” Model of a Loss Incident:
3
4
2
1
Planned activity and its hazards & risks
X
X
X
X
Successive levels of effective control measures
Effective Implementation of a Risk Management Program
D
Successful outcome
A Fresh Perspective: The Block of Swiss Cheese
Chapter 4.4: The Swiss Cheese Model of a Loss Incident

## Slide 11
When there are weaknesses in the Risk Management Program – the program implementation is defective or ineffective – then there are breakdowns in the engineering controls, the administrative controls, and the work-practices, as represented by the holes in the cheeses slices.
The “Swiss Cheese” Model of a Loss Incident:
3
4
2
1
Breakdowns in safeguards and control measures, some due to active failures, some due to root causes.
A Fresh Perspective: The Block of Swiss Cheese
Planned activity and its hazards & risks …
and a successful outcome is intended.
Successful outcome?
Chapter 4.4: The Swiss Cheese Model of a Loss Incident

## Slide 12
It is only a matter of time (probability, likelihood, chance, luck) before all of the breakdowns in the engineering controls, administrative controls, and work practices happen at the same time – these align – and a loss incident happens.
The “Swiss Cheese” Model of a Loss Incident:
3
4
2
1
Planned activity and its hazards & risks
D
Breakdowns in control measures, ultimately due to root causes.
Loss Incident
A Fresh Perspective: The Block of Swiss Cheese
Chapter 4.4: The Swiss Cheese Model of a Loss Incident

## Slide 13
After the root cause analysis is completed and the recommendations that address the root cause(s) are effectively implemented, then the effectiveness of the implementation of the Risk Management Program is restored, and planned activities can be undertaken with successful outcomes.
The “Swiss Cheese” Model of a Loss Incident:
3
4
2
1
Planned activity and its hazards & risks
X
X
X
X
Successive levels of effective control measures
D
Successful outcome
Effective Implementation of a Risk Management Program
A Fresh Perspective: The Block of Swiss Cheese
Chapter 4.4: The Swiss Cheese Model of a Loss Incident

## Slide 14
Chapter 4.5:
Linking Root Causes to the Recommendations
14
Notes: ENGG404 Lecture 00 - Day 1
2012 Fall
14
14

## Slide 15
A basic framework to understand the construct of a root cause analysis.
Causes in the Root Cause Analysis
Category of Cause
Type of Cause
15
Introduction – The Construct of an RCA:
Chapter 4.5: Linking Root Causes to the Recommendations

## Slide 16
Basic Cause
Immediate Cause
Incident Description
Latent Cause
Causes in the Root Cause Analysis
Category of Cause
Type of Cause
16
Introduction – The Construct of an RCA:
Chapter 4.5: Linking Root Causes to the Recommendations

## Slide 17
Engineering Factors Job Factors Personal Factors
Basic Cause
Immediate Cause
Incident Description
Latent Cause
Inadequate Program Inadequate Standards Inadequate Compliance
Causes in the Root Cause Analysis
Category of Cause
Type of Cause
Substandard Work Practice or Substandard Condition
17
Introduction – The Construct of an RCA:
Chapter 4.5: Linking Root Causes to the Recommendations

## Slide 18
Incident
Immediate Cause
Intermediate Cause
Basic Cause
Latent Cause
Weakness in Management System Element #.
Engineering Factors Job Factors Personal Factors
Basic Cause
Immediate Cause
Incident Description
Latent Cause
Inadequate Program Inadequate Standards Inadequate Compliance
Recommendation?
Causes in the Root Cause Analysis
Category of Cause
Type of Cause
Substandard Work Practice or Substandard Condition
Intermediate Cause
18
Introduction – The Construct of an RCA:
Chapter 4.5: Linking Root Causes to the Recommendations

## Slide 19
19
Examine a Root Cause:
Equipment found in defective state
Improper Risk Taking Improper Motivation
Basic Cause
Immediate Cause
Incident Description
Latent Cause
Inadequate Program
Causes in the Root Cause Analysis
Category of Cause
Type of Cause
Sub-standard Work Practice
Management failed to communicate or failed to check that the IM understood Corporate Values: “Safety always before Production”
IM had not yet learned or taken to heart or cared that or understood that safety checks must be done before Prod’n checks
IM prioritized Mtce work on Prod’n Equipment over Safety Equipment
Industrial Mechanic (IM) did not follow / implement procedure
Latent cause?
Colour coding is used here to emphasise cause types.
Colour coding is not necessary for your team project!
Chapter 4.5: Linking Root Causes to the Recommendations

## Slide 20
20
Examine One Root Path in an RCA – Branch Improvements:
Chapter 4.5: Linking Root Causes to the Recommendations
Equipment found in defective state
Industrial Mechanic (IM) did not follow / implement procedure
IM prioritized Mtce work on Prod’n Equipment over Safety Equipment
IM had not yet learned or taken to heart or cared that or understood that safety checks must be done before Prod’n checks
Management failed to communicate or failed to check that the IM understood Corporate Values: “Safety always before Production”
Consider these last two boxes. This root can be drawn better. Where do you see an opportunity to improve the root and what is it?

## Slide 21
21
Examine One Root Path in an RCA – Branch Improvements:
Chapter 4.5: Linking Root Causes to the Recommendations
Equipment found in defective state
Industrial Mechanic (IM) did not follow / implement procedure
IM prioritised Mtce work on Prod’n Equipment over Safety Equipment
IM had not yet learned (i.e. cared for, understood) that safety checks must be done before Prod’n checks
IM was not trained on Corporate Values
Management failed to check that the IM understood Corporate Values: “Safety always before Production” as part of the communications plan.
Management failed to train IM on Corporate Values
The word “OR” in the cause statement is replaced with an OR gate, and two roots result.

## Slide 22
22
Examine Two Roots in an RCA: Latent Causes and Categories
Chapter 4.5: Linking Root Causes to the Recommendations
Equipment found in defective state
Industrial Mechanic (IM) did not follow / implement procedure
IM prioritised Mtce work on Prod’n Equipment over Safety Equipment
IM had not yet learned (i.e. cared for, understood) that safety checks must be done before Prod’n checks
IM was not trained on Corporate Values
Management failed to check that the IM understood Corporate Values: “Safety always before Production” as part of the communications plan.
The management communications plan (program) did not include steps to check that new employees could explain Corporate Values. (LC-S)
Management failed to train IM on Corporate Values
The (existing) training program on Corporate Values was not implemented. (LC-C)
Note the sub-category for the left root latent cause: because the training program exists (the cause states “not implemented”), so one could reasonably infer that this latent cause can be categorized as a “C – Inadequate Compliance with Program Standards”.

## Slide 23
23
Examine Two Roots in an RCA: Latent Causes and Categories
Chapter 4.5: Linking Root Causes to the Recommendations
Equipment found in defective state
Industrial Mechanic (IM) did not follow / implement procedure
IM prioritised Mtce work on Prod’n Equipment over Safety Equipment
IM had not yet learned (i.e. cared for, understood) that safety checks must be done before Prod’n checks
IM was not trained on Corporate Values
Management failed to check that the IM understood Corporate Values: “Safety always before Production” as part of the communications plan.
The management communications plan (program) did not include steps to check that new employees could explain Corporate Values. (LC-S)
Management failed to train IM on Corporate Values
Note the sub-category for the right root latent cause: because the communications plan lacked specific steps to check (and validate) training on Corporate Values, one could reasonably infer that the program exists, but the details (standard) were inadequate; thus, this latent cause can be categorized as an “S – Inadequate Program Standards”.
The (existing) training program on Corporate Values was not implemented. (LC-C)

## Slide 24
Equipment found in defective state
RMSE #1) MLCA
Improper Risk Taking Improper Motivation
Basic Cause
Immediate Cause
Incident Description
Latent Cause
Inadequate Standard
Causes in the Root Cause Analysis
Category of Cause
Type of Cause
Sub-standard Work Practice
Management failed to check that the IM understood Corporate Values: “Safety always before Production” as part of the communications plan.
IM had not yet learned (i.e. carunderstood) that safety checks must be done before Prod’n checks
IM prioritized Mtce work on Prod’n Equipment over Safety Equipment
Industrial Mechanic (IM) did not follow / implement procedure
24
The management communications plan (program) did not include steps to check that new employees could explain Corporate Values. (LC-S)
Examine One Root Path in an RCA: Latent Cause
Note the Latent Cause is stated in unique and specific terms relevant to the loss incident RCA and is aligned with RMSE#1 MLCA
Chapter 4.5: Linking Root Causes to the Recommendations

## Slide 25
Equipment found in defective state
Improper Risk Taking Improper Motivation
Basic Cause
Immediate Cause
Incident Description
Latent Cause
Inadequate Standard
Causes in the Root Cause Analysis
Category of Cause
Type of Cause
Sub-standard Work Practice
Management failed to check that the IM understood Corporate Values: “Safety always before Production” as part of the communications plan.
IM had not yet learned (i.e. carunderstood) that safety checks must be done before Prod’n checks
IM prioritized Mtce work on Prod’n Equipment over Safety Equipment
Industrial Mechanic (IM) did not follow / implement procedure
25
The management communications plan (program) did not include steps to check that new employees could explain Corporate Values. (LC-S)
Examine One Root in an RCA: Latent Cause & Recommendation
Chapter 4.5: Linking Root Causes to the Recommendations
Recommendation!
RMSE #1) MLCA
A recommendation to address this latent cause:
Improve the “Corporate Values” Communications Plan:
  Confirm the organization has established corporate values
  Include steps in the communications plan to confirm that new employees can explain the Corporate Values.
  Implement a job observation audit system so management can confirm alignment to corporate values i.e. that the communications plan is effective.

## Slide 26
To test and identify when you have “drilled sufficiently deep” to identify the latent causes, use the categories and sub-categories from the C&E Model to check of you are at the latent cause, or still at a basic cause.
As will be seen (on page #33 “Effectiveness of Actions to Address Causes & Prevent Recurrence”), the nature of the recommendation can also reveal if you are at a latent cause or still at a basic cause.
Basic Cause
Latent Cause
Weakness in Management System Element #.
Engineering Factors Job Factors Personal Factors
Basic Cause
Latent Cause
Inadequate Program Inadequate Standards Inadequate Compliance
Recommendation?
2
3
4b
4a
5
26
1
Test - Basic Cause or Latent Causes?
Chapter 4.5: Linking Root Causes to the Recommendations

## Slide 27
27
Chapter 4.2: Cause and Effect Models
Chapter 4.3: Root Cause Analysis of an Incident
Example: What is the Recommendation?
Petroleum fire
Petrol released from pump casing
Pump casing corroded (failed)
Casing material was incompatible
Improper material was used
Pump design was incorrect
The engineering work process / program to design pumps at this refinery was inadequate.
LOSS INCIDENT
Incident description
Intermediate
IC: Sub-standard condition
intermediate
intermediate
BC: Design – inadequate tech. design
LC-P: RMSE#7 DC&SU
CATEGORIES
Notes: 27

## Slide 28
28
Note the Effectiveness of Actions on Causes to Prevent Recurrence:
Petroleum fire
Petrol released from pump casing
Pump casing corroded (failed)
Casing material was incompatible
Improper material was used
Pump design was incorrect
The engineering work process / program to design pumps at this refinery was inadequate.
LOSS INCIDENT
Replace the pump. Note: This actions fixes the pump that failed, but not any other pumps in the refinery, now or in the future.
Correct the design specification for pumps in this kind of process service.
Note: This action fixes the design for all pumps in this service, now and in the future, but not any pumps in other services.
Correct the work process for writing specifications / designing pumps for all pumps at this refinery.
Note: This fixes all designs for all pumps in all services.
CORRECTIVE ACTIONS
NO PREVENTION
PREVENTS ONLY SAME SERVICE
PREVENTS ALL PROCESS SERVICES
Chapter 4.5: Linking Root Causes to the Recommendations
Notes: 28

## Slide 29
Chapter 4.6:
Tools for How to Develop & Prioritize Recommendations
29
Notes: ENGG404 Lecture 00 - Day 1
2012 Fall
29
29

## Slide 30
30
Any incident investigation / root cause analysis (your team project) will generate many possible risk reduction solutions.
Management (you) must carefully evaluate these ideas in order to determine which ones are practicable, can be effectively implemented, and be effective when implemented.
Your recommendations should be SMART: specific, measurable, actionable, realistic, and timely.
The process consists of these major steps:
  Generate the Preliminary Recommendations.
  Characterize and Prioritize the Recommendations.
  Do a “Reality Check”.
  Document the Recommendations.
  Summarize the Recommendations.
Developing Key Recommendations:
1)-3) are a “work in progress”
Chapter 4.6: Tools for How to Develop & Prioritize Recommendations
Notes: ENGG404 2015W
21-January-2015
30
30

## Slide 31
You have a number of possible actions / recommendations.
Which recommendations will you implement?
In what order will you implement them?
CONSIDER these objectives of implementing a recommendation:
31
Practicable
Can be Successfully Implemented
Effective Once Implemented
Useful & Feasible
The Challenge of Prioritizing Recommendations:
Chapter 4.6: Tools for How to Develop & Prioritize Recommendations
Notes: 31

## Slide 32
32
Easiest to Implement
Lowest Cost to Implement
Quickest to Implement
Addresses Latent Causes
Most effective
The Best Risk Reduction Solutions Are Those That Are:
Chapter 4.6: Tools for How to Develop & Prioritize Recommendations
Notes: 32

## Slide 33
33
Best approach for quickly prioritizing actions of a straight-forward nature.
Generally want solutions with the lowest effort:
Low Effort
Simple or Known Technology
Low Cost
Quick to Implement
Short Duration
Consider “Effort”:
Chapter 4.6: Tools for How to Develop & Prioritize Recommendations
Notes: 33

## Slide 34
34
Gain refers to:
  The effectiveness of the solutions in addressing the causes (reducing the risk).
    The solution that addresses latent causes is more effective than a solution that addresses basic causes or immediate causes.
Experts input: Typically, the persons with expertise and knowledge of the incident, the technology, the causes, and the scope and nature of the fix can make the best judgment on the effectiveness of the risk reduction solutions.
Consider “Gain”:
Chapter 4.6: Tools for How to Develop & Prioritize Recommendations
Notes: 34

## Slide 35
35
Spending 10 hrs on an assignment that’s worth 0.5% of your mark
Method #1: the Simple Effort v Gain Illustrated:
Chapter 4.6: Tools for How to Develop & Prioritize Recommendations
Notes: 35

## Slide 36
36
Method #2: The Complex Effort v Gain Tool: “Quantitative”
Chapter 4.6: Tools for How to Develop & Prioritize Recommendations
Notes: 36

## Slide 37
37
Method #2: The Complex Effort v Gain Tool: “Quantitative”
GAIN
EFFORT
Chapter 4.6: Tools for How to Develop & Prioritize Recommendations
Notes: 37

## Slide 38
38
Gain Index | Gain Index Criteria (any one of or combination of):
4 | Addresses latent causes. Eliminates hazards or has the greatest reduction in risk levels. Eliminate initiating events.
3 | Addresses basic causes. Reduces risk levels to a lesser extent than “4”. Prevent incident by eliminating subsequent condition splits. Eliminates impact in overall PEAP despite having an event.
2 | Addresses immediate causes. Reduces risk levels to a lesser extent than “3”. Minimizes impact significantly in overall PEAP i.e. mitigates the consequence of an incident.
1 | Minimizes impact slightly in overall PEAP i.e. mitigates the consequence of an incident. Does not address any cause. Reduces risk levels to a lesser extent than “2”, or not at all.
Gain Index of The Complex Tool:
Chapter 4.6: Tools for How to Develop & Prioritize Recommendations
Notes: ENGG404 2015W
21-January-2015
38
38

## Slide 39
39
EFFORT INDEX | 1 (high effort) | 2 | 3 | 4 (low effort)
Practicability (Shown as “Nature of Fix” in the combined table.) | difficult / challenging / develop new technology | apply complex technology | apply simple technology | the solution is not technology
Initial Cost | > $2M | $1M - $2M | $0.1M - $1M | <$100,000
On-going Costs | > 100,000 per year | $100K > cost per year > $10K | <$10,000 per year | no additional on-going cost
Timeline (the time before the action can be implemented) | implemented more than one year | can be implemented within 1 year | can be implemented within 3 months | can be implemented immediately
Duration (the time it takes to put the action into place e.g. MOC, engineering project, planning, communication, training) | requires more than 3 months | requires less than 3 months | requires less than one month | requires less than one week
Frequency (how often does the action need to be repeated) | once per month or more often | once per quarter | once per year | one-time
Effort Index of The Complex Tool:
Chapter 4.6: Tools for How to Develop & Prioritize Recommendations
Notes: 39

## Slide 40
40
Consider the risk reduction solution.
  Gain: “4: Addresses latent causes.”
  Effort: score of 18 (4+3+3+4+1+3)
The total score: 72 = 4 x 18.
EFFORT INDEX | 1 (high effort) | 2 | 3 | 4 (low effort)
Practicability | difficult / challenging / develop new technology | apply complex technology | apply simple technology | the solution is not technology
Initial Cost | > $2M | $1M - $2M | $0.1M - $1M | <$100,000
On-going Costs | > 100,000 per year | $100K > cost per year > $10K | <$10,000 per year | no additional on-going cost
Timeline (the time before the action can be implemented) | implemented more than one year | can be implemented within 1 year | can be implemented within 3 months | can be implemented immediately
Duration (the time it takes to put the action into place e.g. MOC, engineering project, planning, communication, training) | requires more than 3 months | requires less than 3 months | requires less than one month | requires less than one week
Frequency (how often does the action need to be repeated) | once per month or more often | once per quarter | once per year | one-time
Example: Employee Training Program
Chapter 4.6: Tools for How to Develop & Prioritize Recommendations
Notes: ENGG406 2015W
21-January-2015
40
40

## Slide 41
41
The higher the score, the better!
Low Hanging Fruit
Nice To Do
Significant effort for significant gain. Carefully evaluate!
Wasted or sub-optimized resources.
Method #2: The Complex Effort v Gain Tool: “Quantitative”
Chapter 4.6: Tools for How to Develop & Prioritize Recommendations

## Slide 42
42
Excessive time can be spent trying to accurately and precisely determine the likelihood and consequences.
This can detract from efforts to move forward with risk reduction solutions.
How do you balance the amount of time you spend on this?
The more expensive the solution, the more time and expertise needed to evaluate
  “Value Engineering” and “Cost – Benefit Analysis”
Paralysis by Analysis: A Pitfall of Complex Ranking Tools:
Chapter 4.6: Tools for How to Develop & Prioritize Recommendations
Notes: 42

## Slide 43
43
Recommendations are derived from your findings e.g. the latent causes from your RCA.
Recommendations should be: SMART
The work process consists of these major steps:
  Generate the Preliminary Recommendations.
  Prioritize and Characterize Each of the Recommendations. Here is where you use the Complex Effort vs Gain Tool.
  Do a “Reality Check”.
  Document the Recommendations.
  Summarize the Recommendations.
1)-3) are a “work in progress”
Generate the Preliminary Recommendations.
Prioritize and Characterize the Recommendations.
Summarize the Recommendations
Do a “Reality Check”
Document the Recommendations
Work Process to Create the Set of Key Recommendations:
Chapter 4.6: Tools for How to Develop & Prioritize Recommendations
Notes: ENGG404 2015W
21-January-2015
43
43

## Slide 44
The 4 successive barriers of the Swiss Cheese Model to a loss incident (in order of effectiveness) are:
  RM System and Elements,
  Engineering Controls,
  Administration controls, and
  Work Practices.
Latent causes are always linked to a relevant management system element.
The most effective recommendations for actions address or eliminate latent causes, rather than basic or immediate.
Prioritize recommendations for action using the complex gain versus effort tool.
Chapter 4.4: The Relationship Between Latent Causes & Incidents Chapter 4.5: Linking Latent Causes to Recommendations Chapter 4.6: Developing & Prioritizing Recommendations
Summary: